## Slide 1: Types of Pumps
UA Pumps
CH 2 Section 1
Learning Outcome 2

## Slide 2: Two basic classifications of pumps
Positive Displacement
Non-positive Displacement

## Slide 3: Positive Displacement
A Positive Displacement pump discharges a definite quantity of liquid for each operating cycle. Fixed Volume
As the name implies these pumps work on the principle of displacement
Liquid enters the pumps through the suction port and is ejected forcibly out of the discharge port by displacement
Reciprocating Pumps and Rotary Pumps are of this type

## Slide 5: Non-Positive Displacement Pumps
Centrifugal pumps, propeller pumps, and special pumps such as jet pumps and hydraulic rams, etc., are non-positive displacement. Variable Volume
The common characteristic of Non-positive Displacement Pumps is that they do not deliver a specific amount of fluid for every movement of the pump
Their discharge rates are directly affected by the amount of pressure in the systems they are supplying

## Slide 6: Non-Positive Displacement Pumps

## Slide 7: Two basic classifications of pumps
Learning Objective Completed
  Describe two basic classifications of pumps
  Define the categories and list pros and cons
Quick review Concept
  Positive Displacement Pump
    Reciprocating Pumps
    Rotary Pumps
  Non-positive Displacement Pump

## Slide 9: Positive Displacement
A Positive Displacement pump discharges a definite quantity of liquid for each operating cycle. Fixed Volume
As the name implies these pumps work on the principle of displacement
Liquid enters the pumps through the suction port and is ejected forcibly out of the discharge port by displacement
Reciprocating Pumps and Rotary Pumps are of this type

## Slide 10: Reciprocating Pumps
A Reciprocating Pump can be described as a pump that has a backward and forward or upward and downward motion.
Basically two position (No spinning)
An example of this is the Pitcher Pump Fig 2-2

## Slide 11
https://www.youtube.com/watch?v=GIRAm5gaUhg

## Slide 12: Reciprocating Pumps
Can you give any other example?

## Slide 13: Reciprocating Pumps
Air compressors
Boiler feed pumps
Deep well piston pumps (for water or oil)
Hydraulic power pumps
Vacuum pumps
Diaphragm type ditch pumps
Hydrostatic test pumps

## Slide 15: Reciprocating Pump Capacity
Fig 2-3
Capacity can vary by
  Bore size
  Length of stroke
  Number of active pistons
Double Acting Pump
  More check valves
  Move fluid on both ends of stroke
  https://www.youtube.com/watch?v=DXYrJq_fjbI&feature=player_detailpage

## Slide 17: Piston Pump vs. Plunger Pump
Fig 2-4
Both are Reciprocating type of Pumps
Piston Pump
  Piston is shorter than base stroke
  Seal is on the piston
Plunger Pump
  Piston is longer than base stroke
  Seal is on the cylinder

## Slide 19: Diaphragm Pump
Fig 2-5
Reciprocating type of Pump
Utilizes rubber or neoprene in place of piston
Used to remove water from
  Trenches
  Drains
  Places with mud, silt, sand
https://www.youtube.com/watch?v=Y6To-bgL4GE

## Slide 20: Rotary Gear Pumps
The rotary gear pump is a positive displacement pump which discharges fluids in a smooth flow
It is simple in design, has few parts and, like a reciprocating pump, is positive acting
It is called a rotary pump because a rotary motion carries the fluid from the inlet to the outlet.

## Slide 21: Rotary Gear Pumps Uses
Strength is the stability of flow
  Can generate significant pressure
    Thousands of pound under steady state
    Move heavy loads safely
Commonly used for hydraulics
  Backhoes
  Loader
Commonly used on oil burners
Commonly used for refrigerant applications

## Slide 23: Rotary Gear Pump Operation
Fig 2-6
Gears A and B rotate in opposite directions
  One driver gear
  One driven gear
  Clearance is gradually reduced
  Trap fluid between teeth and moved along
  Fluid acts as the seal/lubricant
  https://www.youtube.com/watch?v=YDh2X0cn-3E
  https://www.youtube.com/watch?v=iDAKfAib4bY

## Slide 24: Rotary Gear Pump Variations
Fig 2-7
Different combinations of
  Rotating components
    Meshing Screw
    Lobes
    Slide/Swing Vanes
    Eccentric
Offer stable fluid flow over wide pressure ranges

## Slide 25
  https://www.youtube.com/watch?v=eDTske_nSeI
  https://www.youtube.com/watch?v=MYvbDaHoxRg
  https://www.youtube.com/watch?v=o9re9d-iB5o
  https://www.youtube.com/watch?v=69ah0Jdj1Ag (First 1 min)

## Slide 26: Positive Displacement Pumps
Learning Objectives Completed
  Describe two types of positive displacement pumps
  Explain mechanical function and list common examples of reciprocating pumps
  Explain mechanical function and list common examples of rotary gear pumps
  Quick review Types Positive Displacement Pump
    Reciprocating Pumps
      Piston
        Double Suction
      Plunger
      Diaphragm
    Rotary Pumps

## Slide 28: Non-Positive Displacement Pumps
The common characteristic of non-positive displacement pumps is that they do not deliver a specific amount of fluid for every movement of the pump Variable Volume
Their discharge rates are directly affected by the amount of pressure in the systems they are supplying
Teaser Concept Less Pressure = More Flow

## Slide 29: Non-Positive Displacement Pumps
Types
Centrifugal pumps
Propeller pumps
Special pumps such
  Jet pumps
  Hydraulic rams
  etc.

## Slide 31: Centrifugal Pumps
Most common type of non-positive displacement pump found in piping systems
They can produce up to several thousand feet of head, they can handle liquids up to 1000 degree F, and they can pump abrasives and solids
They have few moving parts and if properly installed and serviced, will last a long time with little maintenance

## Slide 32: Centrifugal Pump

## Slide 33: Centrifugal Pump Quick Note
Oxygen in water will affect the pump material
    The dissolved O2 will react with some materials to form rust
For systems that use potable water frequently
  Material must be resist rust
  Bronze is very common
    Open systems such as domestic feed
For closed systems (Non frequent)
  Material can be susceptible to rust
  Cast Iron is very common

## Slide 34: Centrifugal Pump Quick Note
Chemical Treatment Matters!

## Slide 38: Closed Systems Using Centrifugal Pumps
Hydronic hot water heating
Chilled water
Domestic hot water
Condenser water

## Slide 41: Non-Positive Displacement Pumps
Learning Objectives Completed
  Describe two types of non-positive displacement or centrifugal pumps
  Explain mechanical function and list common examples of centrifugal pumps
  Quick review a Non-positive Displacement Pump is
    Variable Flow
    Dependant on System Pressure
    Can be
      Centrifugal
          Construction material matters if air in system
      Propeller
      Special

## Slide 43: Centrifugal Force
Centrifugal force is the force generated by rotation which acts directly outward from the center of rotation
Examples
  Whirlpool created in the center of spinning liquid
  Automobile tends to move out side on a bank turn
  Merry-go-round

## Slide 44: Centrifugal Force
A centrifugal pump takes its liquid at the center of rotation of the impeller
The liquid is picked up by the impeller vanes and thrown outward, away from the center of rotation, into a casing or volute
The effectiveness of the vanes in a centrifugal pump is improved by shaping them with a curved backward slope

## Slide 45
Fig 2-11

## Slide 46: Centrifugal Force
Fig 2-11
Water remains in bucket even when upside down
What happens when we spin slower?

## Slide 47
Fig 2-12

## Slide 48: Centrifugal Force
Fig 2-12
Same concept but with multiple buckets rotating around a center point
Visualize the bottoms removed. The result is a continuous pressure from the liquid in the buckets against the casing
See the pressure differential potential?

## Slide 49
Fig 2-13

## Slide 50: Centrifugal Force
Fig 2-13
Extend concept: Buckets are now pie shaped
Acts as a paddle wheel
Rotation forces the liquid out against casing

## Slide 52
See the differential potential?
Fig 2-14

## Slide 53: Centrifugal Force
Fig 2-14
Add inlet, outlet and a driver to form a basic centrifugal pump
Liquid picked up by impeller vanes is thrown outward until stopped by a casing or volute

## Slide 55
Fig 2-15
Notice the curve?

## Slide 56
Centrifugal force is a force that pushes a body outward when it is spinning around a center.
Notes: Although there are many variations of centrifugal pump designs, they all employ centrifugal force to operate. Centrifugal force is a force that pushes a body outward when it is spinning around a center. See Figure 4-7.

## Slide 57: Centrifugal Force
Fig 2-15
Design changes to improve efficiency
Change the shape of the vanes to curve backwards
Known as an Impeller

## Slide 58
Notice the curve?

## Slide 59
Fig 2-16

## Slide 60: Centrifugal Pumps
Fig 2-16
The casing of the centrifugal pump expands gradually in the direction of rotation
This gradually expanding passage causes the flow velocity to be reduced as the fluid flows toward the pump discharge connection
This expanding casing, called a volute makes the pump operate more efficiently and gives the name to the volute centrifugal pump which is widely used throughout the piping industry

## Slide 62: Centrifugal Pumps
The velocity head becomes pressure head before the water reaches the circumference of the casing, and flows toward the discharge outlet
The quantity of water pumped depends on the size of the suction and discharge lines, the size of the impeller and its speed

## Slide 63
Centrifugal pump manufacturers have developed many volute and impeller configurations in order to meet the requirements for different applications.
Notes: Centrifugal pumps may be single suction or double suction pumps. They may be base mounted, in which the pump, the bearing assembly, and the motor are all mounted on a common base and ready for installation on a foundation. They may also be in-line pumps intended for installation directly in a pipeline without a base. See Figure 4-13.

## Slide 64: Centrifugal Force
Learning Objectives Completed
  Describe the principles of centrifugal force and how it operates in this type of pump
  Quick review Centrifugal Force
  Theory
  Vocabulary
    Casing
    Volute
    Impeller
Centrifugal Pump Principle 1 (8 min)
https://www.youtube.com/watch?v=w8WcMnUiYQQ

## Slide 67: Centrifugal Impellers
Types
Open
Semi-open
  Web
Enclosed
  Web
  Shroud

## Slide 69: Centrifugal Impellers
Fig 2-17
Open
Consists of blades attached to a hub
Suited to pumping semi solids like sewage

## Slide 70: Centrifugal Impellers
Fig 2-17
Semi-open
Added circular plate called the web
Provides additional support
Allows blades to be thinner
Sandwiches the fluid between the casing

## Slide 71: Centrifugal Impellers
Fig 2-17
Enclosed
Additional circular plate called the shroud
Hold liquid between both pieces
Reduced friction loss for efficient operation

## Slide 76: Centrifugal Impellers
Learning Objectives Completed
  Compare 3 different types of centrifugal impellers
  Quick review Centrifugal Impellers
  Theory
  Vocabulary
    Open
    Semi-open
        Web
    Enclosed
      Shroud
Centrifugal Pump Principle 3 (13 min)
https://www.youtube.com/watch?v=3g_aZLzpRJs

## Slide 78
Centrifugal Pump Priming
Pump Priming videos 4 Min
https://www.youtube.com/watch?v=2FA6t7wHtF0

## Slide 79: Centrifugal Pump Priming
Open systems such as lift stations
Pump starts with air in the impeller
    Very little centrifugal force will be generated
    Therefore very little pressure differential
Water must be allowed to enter to pump
    Air must have a way to escape
This is called Priming

## Slide 80: Centrifugal Pump Priming
Simplest arrangement
  Impeller located below the water level
  In this case the pump will fill automatically
Less favorable arrangement
  Impeller located above the water level
  Casing must be filled by a separate source
    Piped to an empty chamber under pressure
    Manually filled through a priming connection above

## Slide 81: Centrifugal Pump Priming
Learning Objectives Completed
  Define the phrase “pump priming” and explain why it is necessary for centrifugal pumps
  Quick review Centrifugal Pump Priming
  Theory
  Vocabulary
  Priming
Pump Priming Issues videos 4 Min
https://www.youtube.com/watch?v=GrpXdcSfbfA

## Slide 83: Well Pumps
Shallow well
Require a foot valve (check valve)
Have a theoretical maximum lift of 34’
What was the actual maximum for pumps?
Practical suction lift on
  Positive displacement pumps is 22’
  Centrifugal pumps it is 15’

## Slide 86
Notice the check valve?

## Slide 87: Deep Well Pumps
Are Submersible Pumps
Reciprocating Pumps
Jet Pump
Concept is to always keep the suction immersed in the pumping liquid

## Slide 89: Deep Well Pumps
Submersible Pumps
How does a submersible pump retain it’s prime?
Entire pump, including motor, is submersed
Liquid lubricates and cools
Serious damage if well level drops to low
https://www.youtube.com/watch?v=RPpoWfuy_7Y Sewage example

## Slide 90: Deep Well Pumps
Reciprocating Pumps AKA Pump Jack
  Creates suction inside of a drop pipe
  V-belt attached to a gear box
  Rod connects to a plunger down in well
  The cylinder, with plunger, is located below level
Up and down movement makes the upper and lower check valves open and close simultaneously
Operates on principle called Working Head

## Slide 92
https://www.youtube.com/watch?v=kcykqOwDvyc

## Slide 96: Deep Well Pumps
Jet Pumps
Use a suction creating device (the jet fitting)
Discharges to the jet fitting where a partial vacuum is formed by the high velocity fluid discharge from the jet nozzle
After passing through the restriction into the expanding venturi fitting the velocity decreases with a corresponding increase in pressure

## Slide 97
https://www.youtube.com/watch?v=m0xBVMQ3wtw

## Slide 98: Multistage Pumps
A multistage centrifugal pump is essentially a high head or high-pressure pump; it consists of two or more stages, depending on the pressure that is required in the system
Each stage is essentially a separate pump, they are located in the same housing and the impellers are attached to the same shaft
Two or more stages may be found in a single housing

## Slide 100
https://www.youtube.com/watch?v=3IzA0Blvv9s
https://www.youtube.com/watch?v=5v8rj3Pyvds
https://www.youtube.com/watch?v=r4GJ34J0z2g

## Slide 101: Propeller Pumps
Propeller Pumps Types
Axial
    Very similar to an enclosed ship propeller
    Problem low pressure differential
Mixed
    To increase the pressure capability of the propeller pump, it is necessary to have part of the energy imparted to the liquid by centrifugal force
    As the liquid flows through the impeller, it axially moves away from the center or rotation

## Slide 103
https://www.youtube.com/watch?v=6FvePM1Hbl8

## Slide 104: Peripheral Pump
The liquid enters the impeller at its peripheral opposite the suction opening of the pump
The short impeller vane, operating in the channel in the body of the pump, causes the liquid to be thrown away from the center of rotation by centrifugal force
The result is that the liquid flows through the pump in a circular spiral pattern continuously receiving energy and building up pressure as it moves from the suction toward the discharge of the pump

## Slide 107: Other Centrifugal Pumps
Learning Objectives Completed
  Explain the mechanical operation of the following types of pumps: Submersible, Jet, Multistage, Propeller, Peripheral
  Quick review Other Centrifugal Pumps
  Theory
  Vocabulary.
    Well Pump
      Shallow
        Foot Valve
      Deep
      Submersible
      Reciprocating
      Jet
    Propeller
    Perhiprial
https://www.youtube.com/watch?v=B8MV09HF-nY
Quick review of centrifugal pumps with different impellers
Last one looks like a perhiprial

## Slide 109: Checkpoint 1
Assignment 1
Page 9 through Checkpoint 1
Pages 9 through 24
Learning Outcome 2 Completed
  Articulate major pump classifications, and then compare/contrast operational theory with common applications
Review Questions
Classifying Centrifugal pumps 6 Min
https://www.youtube.com/watch?v=TLiBzn3Zlvg
Meant as a review