## Slide 1: Reverse Rim Shaft Alignment
Verti-Zontal Style
Presented by David Zdrojewski
VibrAlign, Incorporated
530 Southlake Blvd
Richmond, VA 23236
804.379.2250

## Slide 2: Why do many companies struggle with shaft alignment?
One issue: they fail to complete a few essential pre-alignment steps

## Slide 3
Essential pre-alignment steps:
http://itunes.apple.com/us/app/align-terms/id541725800?mt=8
Rough Alignment

## Slide 4
Essential pre-alignment steps:
Rough alignment
Obvious soft foot

## Slide 5
Essential pre-alignment steps:
Rough alignment
Obvious soft foot
Tighten in sequence

## Slide 6
Essential pre-alignment steps:
Rough alignment
Obvious soft foot
Tighten in sequence
Final soft foot

## Slide 7
Pre-alignment steps:
Rough alignment
Obvious soft foot
Tighten in sequence
Final soft foot
Clean up
New shims
Check run-out
Pipe stress
Hub separation

## Slide 8
Reverse Rim Dial Measurements:
Set dials to zero @9:00.

## Slide 9
Reverse Rim Dial
Measurements:
Set Dials to zero @9:00.
Rotate the shafts to 3:00.
Set dials to ½ values.

## Slide 10
Reverse Rim Dial Measurement:
Set Dials to zero @9:00.
Rotate the shafts to 3:00.
Set dials to ½ values.
Rotate dials to 12:00.
Record your numbers.

## Slide 11
Reverse Rim Dial
Corrections:
The vertical is either graphed or calculated.
Loosen the bolts.
Make the proper shim corrections.

## Slide 12
RESULTS
Vertical Offset
Stationary
Indicator
Movable
Indicator
Distance Between Indicators (inches)
Movable Indicator to Front Foot (inches)
Front Foot to Back Foot (inches)
Angularity (mils/in)
Offset (mils)
Front Foot Position (mils)
Back Foot Position (mils)

## Slide 13
Reverse Rim Dial
Corrections:
The vertical is either graphed or calculated.
Loosen the bolts.
Make the proper shim corrections.
Leave the bolts loose.
Rotate the dials back to 3:00.
Make the horizontal correction.

## Slide 14
Reverse Rim Dial
Corrections:
The vertical is either graphed or calculated.
Loosen the bolts.
Make the proper shim corrections.
Leave the bolts loose.
Rotate the dials back to 3:00.
Make the horizontal correction.

## Slide 15: www.thealignmentblog.com