## Slide 1: Collecting Data 1. Collect Nameplate Data
You collect Nameplate Data and Fax it to the Predictive Diagnostics Team.
The Predictive Diagnostic Team will create a database for your machines.
Allow 2 days to 1 week for the databases to be completed.
Your routes will be downloaded into the Microlog.

## Slide 2: Collecting Data 1. Collect Nameplate Data
Accurate Speed
You can use a tachometer.
  Contact
  Photo
  Strobe
Or, you can calculate the fan speed.
Fan pulley diameter
Motor pulley diameter
Motor RPM
X
Fan RPM

## Slide 3: Activity 3 Calculating Fan Speed
Calculate the fan speed #1:
The motor pulley diameter is 4”
The fan pulley diameter is 12”
Fan speed =
Calculate the fan speed:
The motor pulley diameter is 10”
The fan pulley diameter is 5”
Fan speed =
Fan pulley diameter
Motor pulley diameter
Motor RPM
X
Fan RPM

## Slide 4: Activity 4: (Optional) Using a strobe to determine machinery RPM
Your Instructor will demonstrate the use of the strobe as a tachometer.
You will be asked to determine the RPM of a machine simulator.

## Slide 5: Collecting Data Where You Take Measurements Pumps:
Bearing Labels:
  MO
  MD
  FI
  FO
Three directions at each bearing:
  IL- In line with belts
  P- Perpendicular to belts
  A- Axial

## Slide 6: Collecting Data Where You Take Measurements Fans:
Bearing Labels:
  MO
  MD
  FI
  FO
Three directions at each bearing:
  IL- In line with belts
  P- Perpendicular to belts
  A- Axial

## Slide 7: Collecting Data Safety:
Lock out tag out
PPE
Cables secure?
Confined Space?
Be aware of surroundings.
If it feels wrong, IT IS!

## Slide 8: Collecting Data Configuring the Microlog, Main Setup

## Slide 9: Collecting Data Configuring the Microlog, Route Setup

## Slide 10: Activity 5: Collecting Vibration Data
Collect vibration data for Fump #1.