## Slide 1: Bump Test
.
A bump test (also called a hammer test) determines the natural frequencies of a machine or a structure.
The idea behind the test is that when an object is impacted or “bumped,” the object's natural or resonant frequencies are excited.
If a spectrum is taken while the object is vibrating due to the impact, spectral peaks result, pinpointing the object's natural frequencies.
A Microlog analyzer can be used to capture this vibration response and to display a spectrum showing the resonant or natural frequencies.

## Slide 2: Bump Test
.
Why Do a Bump Test?
Vibration forces transmitted by rotating machines often excite natural resonances in attached structures. Whenever such structural resonances appear, vibration responses are amplified and can result in fatigue failures. Structural resonances can also mask the cause of a machine's vibration, making it difficult to implement corrective machine maintenance.
Bump tests identify a structure's resonant modes and provide a maintenance engineer the opportunity to change the resonance frequency so as to reduce or eliminate damaging vibration.

## Slide 3: Bump Test
.
To Perform the Bump Test Using the Default Setup\
Attach the accelerometer to the test object (machine case or structure)
From the Analyzer screen, use the arrow keys to highlight the Bump Test icon, and press the Start function button. The measurement is performed and the initial measurement results display.
If you highlight a measurement’s icon and press the Enter (Fire) button instead of the Start function button, you will display the measurement’s setup screen, not start the measurement.

## Slide 4: Bump Test
.
Commence bump test hammer hits to display natural frequency spectral peaks.
Move the spectral cursor to identify natural frequencies.
Average, Stop, Start, and Save function button options operate as previously described in this chapter’s Using the Default Measurement Setup section. Reference this previous section for details.
Bump Test View Options
View - Use the View function button to determine how to view the displayed bump test
measurement results.
View options for bump test measurements include:
FFT for CH1
Power Cepstrum for CH1
Power Spectrum for CH1
FFT+Power Cepstrum for CH1
FFT+Power Spectrum for CH1
Table of peaks for CH1